6502 Architecture
- Modern computer architecture is based off aan architecture called the Van Neumann architecture. It’s divided into two main parts: A) CPU and B) memory.
- Structure of computer memory – Von Neumann architecture also says computer data and programs live In memory. Both are accessed and stored the same way.
- The CPU reads in instructions from memory one at a time and executes them in a fetch-execute cycle. To accomplish this, the CPU contains the following elements:
  - CPU fetches from the program counter (PC) – holds the location of the next instruction to be executed
  - The Program Counter passes on to the instruction decoder – figures out what the instruction means
  - Data is stored and loaded memory locations on the data bus – the physical connection between the CPU and memory.
  - The data bus can host general & special purpose registers – memory locations used by the CPU; general registers can be used for anything while special registers are reserved for specific purposes.
  - Data is then passed to arithmetic/logic unit – decoded instructions are further processed and instructions are executed. After calculations are complete, results are placed on the bata bus in the appropriate locations specified by the instruction.
- The 6502 registers include an 8-bit accumulator (A), two 8-bit general index registers (X, Y), 7 processor status flag bits (P), an 8-bit stack pointer (S), and a 16-bit program counter (PC).
- The stack’s address space is hardwired to memory page $01, i.e., the address range $0100-$01FF (256-511). Software access to the stack is done via four implied addressing mode instructions, whose functions are to push or pop (pull) the accumulator or the process status register. The same stack is also used for subroutine calls via JSR (Jump to Subroutine) and RTS (Return From Subroutine) instructions and for interrupt handling. Since the stack is 16 bit (1 word), it is possible to nest subroutines up to 128 levels deep.
- The processor status (P) is not directly accessible by any 6502 instruction, but have instructions that test the existence of status bits in the register:
  - Bit 7; Negative (N) – set if the accumulator is set
  - Bit 6; Overflow (V) – set if the arithmetic operation produces an invalid signed result. I.e, when adding results in a negative and subtracting results in a positive.
  - Bit 5; unused.
  - Bit 4; Break (B) – set if an interrupt is caused by the BRK instructin, reset if caused by an external interrupt
  - Bit 3; Decimal (D) – set if decimal mode is active. NES does not have a decimal mode.
  - Bit 2; IRQ Disable (I) – set if maskable interrupts are disabled. SEI instruction sets and and the CLI instruction clears.
  - Bit 1; Zero (Z) – set if the result of the last operation was 0.
  - Bit 0; Carry © - set if the last operation caused an overflow from bit 7 (add produced a carry) or an underflow from bit 0 (subtraction produced a borrow).
  - The 6502 has 13 addressing modes; ways of accessing memory:
    - immediate (#FF)- value given is a number to be used immediately by the instruction. For example, LDA #$99 loads the value $99 into the accumulator.
    - absolute (FFFF) – value given is the 16-bit address of a memory location that contains the 8 bit value to be used. For example, STA $3E32 stores the present value of the accumulator in memory location $3E32.
    - Zero page (FF) – The first 256 memory locations ($0000-00FF) are called “zero page”. Instructions making use of zero page save memory by not using an extra $00 to indicate the high part of the address. For example, LDA $0023 works but uses an extra byte; LDA $23 is the zero page address
    - implied - instruction that does not reference memory. For example, CLC just clears the carry flag, DEX just decrements X register by one, TYA transfers the Y register to the accumulator
    - indirect absolute ((FFFF)) – Only used by JMP (jump). It takes the given address and uses it as a pointer to the low part of a 16 bit address in memory, then jumps to that address. For example, JMP ($2345), jump to address in $2345 low and $2346 high. So if $2345 contains $EA and $2346 contains $12, the next instruction executed is the one stored at $12EA.
    - Absolute indexed (FFFF, X) – the final address is found by taking the given address as a base and adding the current value of the X or Y register to it as an offset. For example, LDA $F453, X where X contains 3. Load the accumulator with the contents of address $F453 + 3 = $F456.
    - Zero page indexed (FF, X) – same as absolute indexed but the given address is in the zero page thereby saving a byte of memory
    - indexed indirect ((FF, X)) – find the 16-bit address starting at the given location plus the current X register. The value is the contents of that address. For example, LDA ($B4, X) where X contains 6. This equates to $BA. If $BA and $BB contains $12 and $EE respectively, then the final address is $EE12.
    - Indirect indexed ((FF), X) – Find the 16 bit address contained in the given location (and the one following). Add to the contents of the given register, fetch the value stored at that register. For example, LDA ($B4), Y – where Y contains 6. If $B4 contains $EE and $B5 contains $12 then the value at memory location $12EE + Y (6) = $12F4 is fetched and put in the accumulator
    - relative (assembler labels) – branch instructions use relative addressing. The next byte is a signed offset from the current address and the net sum is the address of the next instruction execute. For example, BNE $7F (branch on zero flag reset) will add 127 to the current program counter (address to execute) and start executing the instruction at that address.
    - Accumulator - the object of the instruction is the accumulator and need not be specified.