6502 Architecture
- Modern computer architecture is based off aan architecture called the Van Neumann architecture. It’s divided into two main parts: A) CPU and B) memory.
- Structure of computer memory – Von Neumann architecture also says computer data and programs live In memory. Both are accessed and stored the same way.
- The CPU reads in instructions from memory one at a time and executes them in a fetch-execute cycle. To accomplish this, the CPU contains the following elements:
  - CPU fetches from the program counter (PC) – holds the location of the next instruction to be executed
  - The Program Counter passes on to the instruction decoder – figures out what the instruction means
  - Data is stored and loaded memory locations on the data bus – the physical connection between the CPU and memory.
  - The data bus can host general & special purpose registers – memory locations used by the CPU; general registers can be used for anything while special registers are reserved for specific purposes.
  - Data is then passed to arithmetic/logic unit – decoded instructions are further processed and instructions are executed. After calculations are complete, results are placed on the bata bus in the appropriate locations specified by the instruction.
- The 6502 registers include an 8-bit accumulator (A), two 8-bit general index registers (X, Y), 7 processor status flag bits (P), an 8-bit stack pointer (S), and a 16-bit program counter (PC).
- The stack’s address space is hardwired to memory page $01, i.e., the address range $0100-$01FF (256-511). Software access to the stack is done via four implied addressing mode instructions, whose functions are to push or pop (pull) the accumulator or the process status register. The same stack is also used for subroutine calls via JSR (Jump to Subroutine) and RTS (Return From Subroutine) instructions and for interrupt handling. Since the stack is 16 bit (1 word), it is possible to nest subroutines up to 128 levels deep.
- The processor status (P) is not directly accessible by any 6502 instruction, but have instructions that test the existence of status bits in the register:
  - Bit 7; Negative (N) – set if the accumulator is set
  - Bit 6; Overflow (V) – set if the arithmetic operation produces an invalid signed result. I.e, when adding results in a negative and subtracting results in a positive.
  - Bit 5; unused.
  - Bit 4; Break (B) – set if an interrupt is caused by the BRK instructin, reset if caused by an external interrupt
  - Bit 3; Decimal (D) – set if decimal mode is active. NES does not have a decimal mode.
  - Bit 2; IRQ Disable (I) – set if maskable interrupts are disabled. SEI instruction sets and and the CLI instruction clears.
  - Bit 1; Zero (Z) – set if the result of the last operation was 0.
  - Bit 0; Carry © - set if the last operation caused an overflow from bit 7 (add produced a carry) or an underflow from bit 0 (subtraction produced a borrow).